### Hardware & Wiring Guide
This guide lists the necessary components and provides a clear wiring plan for connecting everything to the ESP32 development board. The most critical aspect of this setup is understanding the 3.3V logic level of the ESP32.
#### 1. Required Components
- Microcontroller: 1 x ESP32 Development Board (e.g., ESP32-WROOM-32 DevKitC, NodeMCU-32S, or similar). An optional ESP32 Breakout Board/Shield is highly recommended to simplify connections.
- Stepper Motor & Driver: 1 x 28BYJ-48 5V Stepper Motor with its corresponding ULN2003 Driver Board. These are typically sold as a kit.
- Real-Time Clock: 1 x DS3231 RTC Module. Ensure it has a CR2032 coin cell battery installed for backup power.
- Power Supplies:
  - 1 x USB Cable (Micro-USB or USB-C) to power the ESP32 board. A standard phone charger or computer USB port is sufficient.
  - 1 x External 5V Power Supply to power the stepper motor driver. A 5V adapter with at least 1A (1000mA) is recommended; a 5V 2A adapter is ideal for ensuring stability.
- Wiring & Prototyping:
  - Jumper Wires (Female-to-Female, Male-to-Female, Male-to-Male as needed).
  - Decoupling Capacitors (Recommended for Stability):
    - 1 x 100nF (0.1µF) ceramic capacitor (often marked "104") for the RTC module.
    - 1 x 10µF to 100µF electrolytic capacitor for the motor driver's power input.
#### 2. Wiring Diagram & Instructions
This plan uses two separate power sources for maximum stability: the ESP32 is powered via USB, and the motor is powered by the external 5V supply.
CRITICAL: COMMON GROUND All components must share a common ground reference. This means a GND pin from the ESP32 must be connected to the GND of the external 5V power supply that powers the motor driver.
Step-by-Step Connections:
1. Power the ESP32: Connect the ESP32 to your computer or a USB wall adapter using its USB port.
2. Power the Stepper Motor Driver:
  1. Connect your external 5V power adapter to the ULN2003 driver board's power input.
    1. + (or VCC) on the ULN2003 -> Positive (+) terminal of your 5V external supply.
    2. - (or GND) on the ULN2003 -> Negative (-) terminal / Ground of your 5V external supply.
  2. Add Decoupling Capacitor: Place the 10µF-100µF electrolytic capacitor across the + and - terminals of the ULN2003 driver board. Ensure the capacitor's negative lead (marked with a stripe) goes to GND (-).
3. Connect the Stepper Motor: Plug the 5-pin connector from the 28BYJ-48 motor into the corresponding socket on the ULN2003 driver board. It is keyed and should only fit one way.
4. Connect the RTC Module to the ESP32:
  1. RTC VCC -> ESP32 3V3 pin. (Powering from 3.3V ensures logic level compatibility).
  2. RTC GND -> ESP32 GND pin.
  3. RTC SDA -> ESP32 GPIO 21 (Standard I2C Data pin).
  4. RTC SCL -> ESP32 GPIO 22 (Standard I2C Clock pin).
  5. Add Decoupling Capacitor: Place the 100nF (0.1µF) ceramic capacitor across the VCC and GND pins of the RTC module, as close to the module as possible.
5. Connect the Stepper Driver to the ESP32:
  1. ULN2003 IN1 -> ESP32 GPIO 19 (Example pin)
  2. ULN2003 IN2 -> ESP32 GPIO 18 (Example pin)
  3. ULN2003 IN3 -> ESP32 GPIO 5 (Example pin)
  4. ULN2003 IN4 -> ESP32 GPIO 17 (Example pin)
  5. (These pins can be changed in the code, but they are good choices as they are not typically used for other special functions).
6. Establish Common Ground (Final, Crucial Step):
  1. Run a single jumper wire from any GND pin on the ESP32 to the - (GND) terminal on the ULN2003 driver board (where the external power supply's ground is connected).
Your hardware is now correctly wired for the ESP32-based web-controlled system.